## Slide 1: SMART INDIA HACKATHON 2025
TITLE PAGE
‣ Problem Statement ID 48 (internal round)
‣ Problem Statement Title AI-Driven Life Cycle Assessment (LCA) Tool for Advancing Circularity and Sustainability in Metallurgy and Mining
‣ Theme Miscellaneous (Sustainability)
‣ PS Category Software
‣ Team ID ________________
‣ Team Name ________________
Idea: DhatuChakra (धातुचक्र) — हर टन का हिसाब · every tonne, accounted for

## Slide 2: IDEA TITLE
Proposed Solution (Describe your Idea/Solution/Prototype) · How it addresses the problem · Innovation and uniqueness of the solution
Your Team Name
WHAT IS LCA?
Life Cycle Assessment totals a product's environmental cost across its life. Core method: Impact = Σ (quantity × emission factor). We compute it cradle-to-gate, per tonne of metal.
WHAT IS CIRCULARITY?
How much material loops back (scrap, recycling) instead of being mined and landfilled. Scored 0→1 by the Material Circularity Indicator (Ellen MacArthur): 0 = fully linear, 1 = fully circular.
WHY METALS, WHY NOW?
Metals ≈ 8% of global CO₂. India: circular-economy policy + National Critical Mineral Mission. EU CBAM taxes embedded carbon in steel/aluminium exports from 2026.
DhatuChakra (धातुचक्र) — AI-assisted LCA & circularity engine for Indian metals: 5 inputs in, ISO-14044-style answers out.
▸ Demo video: <add link>
▸ Documentation: LCA-TOOL/docs · technical PDF
▸ Code + prototype: github.com/grv-io/LCA-TOOL
THE PROBLEM → OUR SOLUTION
• Conventional LCA is out of reach: 25+ parameters, database licences ≈ €4,000/yr, weeks of consultants — most Indian plants skip it
• DhatuChakra needs 5–8 inputs or one plain sentence ("aluminium smelter in Odisha, 40% scrap") → full profile in seconds
• AI fills the missing parameters with visible confidence scores — estimates flagged, never hidden, always overridable
• Output per tonne: GWP · energy · water · acidification + MCI, live linear-vs-circular compare, auditable PDF report
INNOVATION & UNIQUENESS
• Not a black box: every figure traces to a cited public source (CEA, IAI, worldsteel, EF 3.1) — shown in-app
• India-first: clickable state-grid map (Himachal 0.18 → Chhattisgarh 0.92 kg CO₂/kWh) + CBAM export cost in ₹ crore
• Real statistics, real ML: 1,000-run Monte Carlo (p05–p95 on every result) + k-NN imputer with honest confidence
• ₹0 data cost: built entirely on free public inventories — no ecoinvent licence anywhere
Verified: recycled aluminium = 16.6 → 0.92 t CO₂e/t (−94%), inside IAI published ranges.

## Slide 3: TECHNICAL APPROACH
Technologies to be used (programming languages, frameworks, hardware) · Methodology and process for implementation (Flow Charts / Images / working prototype)
Your Team Name
STACK
Frontend Next.js · TypeScript · Tailwind · Recharts · Plotly (Sankey)
Backend Python FastAPI · Pydantic · PostgreSQL
LCA engine factor-matrix calc · EMF MCI v3 · Brightway2.5-ready
AI / ML LightGBM quantile imputer (p10–p90 confidence) · surrogate regressor R² > 0.95, < 20 ms · NumPy Monte Carlo (1,000 runs)
LLM Claude API — plain text → scenario JSON + grounded recommendations
Reports Jinja2 → WeasyPrint PDF
Deploy Docker · Render · Vercel
Prototype today: client-side HTML/JS, offline — 3 metals, India state map, k-NN imputer (500 scenarios), 1,000-run Monte Carlo, CBAM, Hindi UI.
How a query flows
User input
5 fields — or one plain-English sentence
LLM parser
text → structured scenario JSON
AI imputer
fills 25+ params + confidence score
LCA engine
quantities × emission factors
AI layer
Factor library (India-first): IAI · worldsteel · CEA CO₂ Baseline · EF 3.1 · IDEMAT — every factor cited (source · year · region)
Monte Carlo
1,000 runs → p05–p95 ranges + histogram
Results / tonne
GWP · energy · water · acidification + MCI chakra
Dashboard & report
Sankey · compare sliders · recommendations · PDF
IMPLEMENTED TODAY ✓
3 metals · 6 scenarios · state-grid map · k-NN imputer · 1,000-run Monte Carlo · CBAM ₹ calculator · MCI chakra · benchmarks · Hindi UI · report — offline, zero backend
FULL BUILD (planned, spec ready)
Brightway2.5 matrix LCA · LightGBM imputer · LLM parser · FastAPI + PostgreSQL — full details: technical PDF · demo video — <add link>

## Slide 4: FEASIBILITY AND VIABILITY
Analysis of the feasibility of the idea · Potential challenges and risks · Strategies for overcoming these challenges
Your Team Name
WHY THIS IS BUILDABLE
• 100% free data — IAI, worldsteel, CEA, EF 3.1, IDEMAT: no paid-licence blocker anywhere in the pipeline
• Working prototype live — 3 metals, state-grid map, k-NN imputer, Monte Carlo, CBAM, Hindi UI; full-build plan written
• ML needs no scarce dataset — the imputer trains on physics-generated scenarios from our own engine
Validated against published values (t CO₂e / t metal):
Route | Ours | Published range
Aluminium — primary (IN grid) | 16.6 | 16–20 (IAI)
Aluminium — recycled | 0.92 | 0.5–1.5 (IAI)
Steel — BF-BOF | 2.19 | 1.9–2.4 (worldsteel)
Steel — EAF (scrap) | 0.70 | 0.4–1.0 (worldsteel)
Copper — primary | 4.24 | ≈4.2 (EF 3.1, indic.)
Challenge / Risk | Strategy
LCI data gaps for Indian plants | Curated 100+ factor table, every row cited (source · year · region); fallback chain IN → world average
Wrong numbers = zero credibility | Validation suite vs IAI / worldsteel published values runs on every change; < 10% error target
“AI is a black box” objection | Confidence score on every estimate + provenance table + uncertainty ranges on screen
Users can't fill 25+ parameters | Plain-English entry + AI imputation — only 5–8 inputs needed
Scope creep in hackathon time | v1 scope locked and SHIPPED: 3 metals, 4 impact categories; Brightway2.5 swap reserved for full build

## Slide 5: IMPACT AND BENEFITS
Potential impact on the target audience · Benefits of the solution (social, economic, environmental, etc.)
Your Team Name
−94%
CO₂ on the recycled aluminium route — 16.6 → 0.92 t CO₂e per tonne
≈ 4.9 t
CO₂e/t removed by a 50% renewable PPA on a primary Al smelter (India grid)
₹0 · minutes
database cost & assessment time — vs €4k/yr licences and weeks of consulting
WHO GAINS
• Metal producers & MSMEs — LCA answers in minutes; decide scrap %, energy sourcing and routes with numbers, not guesses
• Ministry of Mines & regulators — standardised, comparable, auditable plant data; supports the National Critical Mineral Mission and circular-economy policy
• Exporters — EU CBAM's definitive regime starts 2026: embedded-emissions reporting for steel & aluminium exports becomes mandatory — exactly what this tool produces
BENEFITS
• Environmental — quantifies the shift to circular routes; pinpoints hotspot stages (smelting ≈ 62% of primary-Al footprint)
• Economic — saves licence + consultant costs; higher circularity = lower import dependence on ore & energy
• Social — small plants get the same analysis capability as corporates; methodology fully transparent
• Strategic — an India-first open emission-factor library becomes reusable national infrastructure

## Slide 6: RESEARCH AND REFERENCES
Details / Links of the reference and research work
Your Team Name
RESEARCH & DATA SOURCES
1. ISO 14040 / 14044 — LCA principles, requirements & guidelines · iso.org
2. Ellen MacArthur Foundation — Material Circularity Indicator methodology v3 · ellenmacarthurfoundation.org
3. International Aluminium Institute — LCI data & GHG pathways · international-aluminium.org
4. worldsteel — Life Cycle Inventory methodology report · worldsteel.org
5. CEA CO₂ Baseline Database v19 — India grid emission factor · cea.nic.in
6. US LCI (NREL) / EU EF 3.1 · ELCD — lcacommons.gov · eplca.jrc.ec.europa.eu
7. IDEMAT 2024, TU Delft — open LCI factors · idematapp.com
8. IBM Indian Minerals Yearbook — Ministry of Mines · ibm.gov.in
9. EU CBAM Regulation 2023/956 — carbon reporting for metal imports · taxation-customs.ec.europa.eu
10. NITI Aayog — circular-economy strategy papers for metals · niti.gov.in
OUR LINKS
▸ Demo video: <add link>
▸ Documentation (PDF): LCA-TOOL/docs/DhatuChakra_Documentation.pdf
▸ Code + prototype: github.com/grv-io/LCA-TOOL
REPRODUCIBLE BY DESIGN
Every number in this deck — 16.6, 0.92, 2.19, 0.70 t CO₂e/t, MCI 0.16→0.83, 62% electricity share — is computed from the sources listed; formulas and validation are in the linked technical PDF.